## Slide 1: MultiGPU programming
Presenter: Jiri Kraus (NVIDIA) Suraj Prabhakaran ¦ April 9, 2014 | 
German Research School for Simulation Sciences GmbH Laboratory for Parallel Programming | 

## Slide 2: Using Multi GPUs
Further speedup computations
Single GPU memory not sufficient
Increases performance/W
Intra-node Multi-GPU
  Easy-to-use, directly use the CUDA API
Inter-node Multi-GPU
  Network communication with MPI

## Slide 3: Application scenario
network
GPU
GPU
core
core
core
core
GPU
GPU
core
core
core
core

## Slide 4: Application scenario
network
GPU
GPU
core
core
core
core
GPU
GPU
core
core
core
core

## Slide 5: Intra-node Multi-GPU
Single CPU thread access Multiple GPUs
CUDA calls issued to current GPU
cudaSetDevice(x) sets the current GPU.
Example
  cudaSetDevice(0);
  cudaMalloc(dst_0,…);
  cudaMemcpy(dst_0, …);
  cudaSetDevice(1);
  cudaMalloc(dst_1,…);
  cudaMemcpy(dst_1, …);

## Slide 6: Intra-node Multi-GPU
Current GPU can be changed even when async calls (kernels, async memcopies) are running
Example
  cudaSetDevice(0);
  kernel<<<…>>>(…);
  cudaSetDevice(1);
  cudaMemcpyAsync(…);

## Slide 7: Multi-GPU Matrix Multiplication
C
A
B
C0
B
A0
Split A and C into two sets of rows
C1
B
A1
=
=
=
x
x
x
GPU 0
GPU 1

## Slide 8: Exercise: Multi-GPU Matrix Multiplication
Use Multiple GPUs to speed up Simple Matrix Multiplication
Split A into 2 set of rows
Verify with NVVP that two GPUs are used.
GPU
GPU
CPU
A0 * B = C0
A1 * B = C1
A0, B
A1, B
C1
C0

## Slide 9: Intra-node Multi-GPU Communication
One GPU has to access data from another GPU
Traditional method: Go about it through the CPU/Main Memory
Due to UVA: Peer-to-peer memcopies (GPUDirect P2P)

## Slide 10: Intra-node Multi-GPU Communication
Check if the GPU can access Peer device
  cudaDeviceCanAccessPeer(&accessible, dev_x, dev_y);
First enable Peer-to-peer communication
cudaDeviceEnablePeerAccess(peer_device,0);
Transfer data between two devices
cudaMemcpy(dst, src, size, cudaMemcpyDeviceToDevice);
    Also works if peer access is not possible or not enabled (fall back with host memory staging)

## Slide 11: Exercise:
Compare memcopies between two devices using:
  Manual staging through main memory
  Using GPUDirect Peer to Peer